Transparent commands – example

Purpose:

To stress importance of Transparent commands.

Example:

How to start Fix straight at the very first chainage with Existing ground level and specify gradient up to some chainage.

Procedure:

- Select Fix straight(by two points) from within Create by Layout... menu

- use Set Profile chainage along an Alignment and Level from Surface: ´SSE

- you will be prompted for: Profile view and Surface to define level. Then select chainage along Alignment – in our case very first chainage or it can be typed in via keybord. Then hit Esc to finish with this Transparent command.

- To specify End point, please select Gradint and chainage in Profile view: ´PGS

- Specify gradient in percentage (+ for up, - for down) and chainage either in Profile view graphicaly or numericaly via keyboard